cONTRIBUTION:	nTCO0XX 		 			 2000 06 12

working Group:	Network Working Group

title:	Roaming issues – the u.s. environment

Issues Addressed:	This contribution provides an overview of the CMRS-IXC interconnection environment  within the United States. The protocols used to transfer a call from the CMRS provider to the IXC would appear to provide a suitable reference point with respect to the long-term evolutionary requirements for the LEC-IXC interface in Canada.

Source:	Clearnet Communications Inc.
Bohdan Zabawskyj

Director, Research and Development

200 Consilium Place, Suite 1600		
Scarborough, Ontario

Tel: 	416 684-3163

Fax: 	416 684-0163

Distribution:	NTWG Interested Parties

REFERENCE:

FILE NAME:	NTCO0XX_BKZ.DOC

Notice:	This contribution has been prepared by Clearnet Communications Inc. (Clearnet) to assist the Network Working Group as basis for discussion. This should not be construed as a binding proposal on Clearnet. Specifically, Clearnet reserves the right to provide amendments, modifications or to withdraw of this contribution at any time.

1.	Introduction

This contribution provides an overview of the CMRS (Commercial Mobile Radio Service)-IXC interconnection environment within the United States.  The protocols used to transfer a call from the CMRS provider to the IXC would appear to provide a suitable reference point with respect to the long-term evolutionary requirements for the LEC-IXC interface in Canada.

2. 	Analysis of anticipated call scenarios

The anticipated call scenarios which may involve an IXC include:

(1)	Calls which are originated from cellular subscribers which are being served by the home system.  This scenario is depicted in Figure 1.

(2)	Calls which are originated from cellular subscribers which are being served outside of the home system.  This scenario is depicted in Figure 2.

2.1	Analysis of Called Number, ANI, and ANI II digit pair information received by the IXC in the anticipated call scenarios

Based on an examination of the Called Number, ANI (Charge Number) and ANI II digit pair (OLI) information which would be received by the IXC for each of the three anticipated call scenarios (described in Tables 1 and 2) it would appear that the received ANI II digit pair or OLI information in conjunction with the received ANI information provides sufficient information for the purpose of uniquely identifying a wireless subscriber and invoking a wireless specific rating plan.

3.	Conclusions

Based on the existing roaming environment in the United States, the information received by the IXC from the CMRS provider - which includes the wireless subscriber's ANI information as well as a wireless-specific ANI II digit pair or OLI information - would provide sufficient information for the purpose of uniquely identifying a specific wireless client and invoking a wireless specific rating plan.

Figure 1: 	Case (a) - A call is originated from a cellular subscriber which is being served by the home serving system (i.e. the subscriber is not roaming)

Table 1: 	Case (a) - Information received by the IXC in the case that a call is originated from a cellular subscriber which is being served by the home serving system

| Information received by IXC | Called Number | ANI (MF) or Charge Number (ISUP) | ANI (MF) or Originating Line Info (ISUP) |
| --- | --- | --- | --- |
| For call originated by subscriber X within system X | AAA-AAA-AAAA | XXX-XXX-XXXX | 62 |
| For call originated by subscriber Y within system Y | AAA-AAA-AAAA | YYY-YYY-YYYY | 62 |

Figure 2: 	Case (b) - A call is originated from a cellular subscriber which is being served outside of the home system (i.e. the cellular subscriber is roaming)

Table 2: 	Case (b) - Information received by the IXC in the case that a call is originated from a cellular subscriber which is being served outside the home system

| Information received by IXC | Called Number | ANI (MF) or Charge Number (ISUP) | ANI (MF) or Originating Line Info (ISUP) |
| --- | --- | --- | --- |
| For call originated by subscriber X within system Y | AAA-AAA-AAAA | XXX-XXX-XXXX | 62 |
| For a call originated by subscriber X within system Z | AAA-AAA-AAAA | XXX-XXX-XXXX | 62 |
| For call originated by subscriber Y within system X | AAA-AAA-AAAA | YYY-YYY-YYYY | 62 |